## Slide 1: Network Verification
Nikolaj Bjørner
Lipari Summer School 2017

## Slide 2: Goals of Tutorial
Motivate: Why this may be an important inter-disciplinary field that can have real impact
Expose: Networking audience to verification ideas and terminology
Survey: Describe and put in context existing work in network verification
Inspire: Resources available, lessons for you to attempt network verification tasks

## Slide 3
Inflection Point: Rise of services, data centers, SDN, NFV
Ideas: Adapt Verification (analysis) & optimization (synthesis)
Intellectual Opportunity: Rethink existing techniques.
Exploit domain structure
Systems Opportunity Working chips with billions of gates.
Why not large operational networks next?
Main Takeaways

## Slide 4: Acknowledgments
George Varghese: Based on joint SIGCOMM 2015 tutorial. Updated with recent results.
Slides borrowed from many sources, including
  Marco Canini, Nate Foster, Brighten Godfrey, Peyman Kazemian, Dejan Kostic, Sharad Malik, Nick McKeown, Mooly Sagiv, Ragunathan, Jennifer Rexford
  Apologies for missing any work related to network verification.

## Slide 5: Why? Look at Networks today
1001
P1
P2
10* P1
1*  P2
,P2
SQL
Drop SQL
Load balancing
Access Control Lists (ACLs)
Multiple Protocols: 6000 RFCs (MPLS, GRE . . .)
Multiple Vendors: Broadcom, Arista, Cisco, . . .
Manual Configurations: Additional arcane programs kept working by “masters of complexity” (Shenker)
Crude tools: SNMP, NetFlow, TraceRoute, . . .
Notes: But to understand why correct design is hard it is important to see even why just understanding ordinary working networks such as lurk behind your Caltech firewall is hard.

## Slide 6: Simple questions hard to answer today
  Which packets from A can reach B?
  Is Group X provably isolated from Group Y?
  Is the network causing poor performance or the server? Are QoS settings to blame?
  Why is my backbone utilization poor?
  Is my load balancer distributing evenly?
  Where are there mysterious packet losses?
Notes: As a result, even simple questions about a network are hard to answer.

## Slide 7: Motivation to do better
Internal: > 1 hr customer visible outage/quarter (P. Patel)
  Azure: 30,000 cores down 3 hrs, L2/L3 configuration bug
  Bing: Entire data center, 8 hours, L2/L3 configuration bug
External: (2012 NANOG Network Operator Survey):
  35% > 25 tickets per month, > 1 hour to resolve
  Amazon, BigDaddy, United Failures (NetCore paper)
  Welsh: vast majority of Google “production failures” due to “bugs in configuration settings”
As we migrate to services ($100B public cloud market), network failure a debilitating cost.

## Slide 8: Networks Tomorrow
Opportunity for custom design optimized networks
Potential simplifications but hard to get right
Online services |  | latency, cost sensitive
Merchant Silicon |  | Build your own router
Rise of Data centers |  | Custom networks
Software defined Networks (SDNs) |  | Program custom design “routing”
P4 (next generation SDN) |  | redefine hardware forwarding at runtime

## Slide 9: Industry
Microsoft: Using Z3 for checking ACLs and forwarding, large scale simulation
Amazon WS: Compliance and customer ACLs
forwardnetworks.com: Startup based on HSA
veriflow.net: Startup based on Veriflow
IntentionNet: Startup based on BatFish
Other players: Cisco, Google, Toga Networks

## Slide 10
Does the network meet auditing criteria?
Do flows take shortest paths, meet redundancy?
What is impact of a change?
Is network fault tolerant?

## Slide 13
Auditing &
Compliance
SecGuru
Karthick
@ Microsoft
Teme & Formal Methods group
@ Amazon

## Slide 14: Digital Hardware Design as Inspiration?
Specification
Functional Description (RTL)
Testbench & Vectors
Functional Verification
Logical Synthesis
Static Timing
Place & Route
Design Rule Checking (DRC)
Layout vs Schematic (LVS)
Parasitic Extraction
Manufacture
& Validate
Specification
Policy Language, Semantics
Testing
Verification
Synthesis
Performance verification?
Network Topology Design
Static checking (local checks)
Wiring Checkers
Interference estimation?
Dynamic checkers/ debuggers
Electronic Design Automation
(McKeown SIGCOMM 2012)
Network Design Automation
(NDA)?
Notes: Inspired by Nick slide on left but we want to think through to a deeper extent what was a direction pointed to by Nick

## Slide 15: This Tutorial’s Slice of NDA
Won’t discuss debugging, very little of run-time verification
Mostly interested in where formal methods can help
Specification
Policy Language, Semantics
Testing
Verification
Synthesis
Notes: Inspired by Nick slide on left but we want to think through to a deeper extent what was a direction pointed to by Nick

## Slide 16: This Tutorial’s Slice of NDA
Specification
Policy Language, Semantics
Testing
Verification
(e.g. reachabilty)
Synthesis
(e.g. forwarding)
Won’t discuss debugging, very little of run-time verification
Mostly interested in where formal methods can help
CTL, NoD, Klee Assert
NetKAT, NetCore
Data Plane: Anteater, VeriFlow, HSA, Atomic Predicates,
First-order + Transitive Closure, local checks
Control Plane: VeriCon, BatFish
One big switch, VLAN, NetCore, NetKAT, FlowLog
NICE, ATPG
Notes: Inspired by Nick slide on left but we want to think through to a deeper extent what was a direction pointed to by Nick

## Slide 17: Road Map
Introduction to Formal Methods
Data Plane Verification
  One counterexample
  All counterexamples
  Optimizations
  Adding Functionality
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 18: INTRODUCTION TO FORMAL METHODS FOR Networking
Introduction to Formal Methods
Data Plane Verification
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 19: Verification: Values and Obstacles
 | Hardware | Software | Networks
 | Chips | Devices (PC, phone) | Service
Bugs are: | Burned into silicone | Exploitable, workarounds | Latent, Exposed
Dealing with bugs: | Costly recalls | Online updates | Live site incidents
Obstacles to eradication: | Design Complexity | Code churn, legacy, false positives | Topology, configuration churn
Value proposition | Cut time to market | Safety/OS critical systems, Quality of code base | Meet SLA, Utilize bandwidth, Enable richer policies

## Slide 20: Main Idea: Network as a Program
Model header as point in high dimensional space and all networking boxes as transformers of header space
Packet
Forwarding
1
2
3
0xx1..x1
Match
+
Send to port 3
Rewrite with 1xx011..x1
Action
11xx..0x
+
Send to port 2
Rewrite with 1x01xx..x1
ROUTER ABSTRACTED AS SET OF GUARDED COMMANDS
NETWORK BECOMES A PROGRAM CAN USE PL METHODS
FOR VERIFICATION, TESTING, AND SYNTHESIS

## Slide 21: Semantics Based Landscape (partial)
Hoare style proofs (1960s-1980s): axioms, inference rules, invariants. Scale? Code churn?
Model checking: search algorithmically over state space to check P. e.g., NuSMV, Impact, IC3
Proof Assistants: Humans help but system can check proofs. E.g., Coq, Isabelle.
Testing: Symbolic execution to maximize coverage and check property failures (e.g., Klee, SAGE)
Notes: To put some perspective into what we do in Header Space Analysis, I need to give you some background on proof techniques used in computing systems, starting with programs and soon extended to hardware verification. M. Talupur: model checking will replace simulation for 50% of units

## Slide 22
Ex: Approaches for Token Passing
Token
Inductive Invariant I: Exactly 1 token at
Node or Link (also correctness spec)
Proof Assistant : Show each action maintains I
Algorithmic Search: Want to show for all states reachable from s0 that
there is exactly 1 Token in every state.
Testing: Generate executions to exercise every action.
A
Program: Receive & Send Token
Initially: s0 token is at A

## Slide 23: Pros and Cons
Model checking: SPIN, nuSMV, Impact, IC3
  Pros: “push-button verification”;
  Cons: finite state systems (e.g., fixed network). Hard to scale (needs abstraction, compression)
Proof Assistants: Coq, Isabelle.
  Pros: Much harder work (must supply invariants)
  Cons: works for infinite state systems (e.g., all networks) and ideally needs methods to suggest invariants
Testing:
  Pros: Can uncover bugs in large code without models
  Cons: Incomplete (state space too large), imprecise
Notes: To put some perspective into what we do in Header Space Analysis, I need to give you some background on proof techniques used in computing systems, starting with programs and soon extended to hardware verification. M. Talupur: model checking will replace simulation for 50% of units

## Slide 24: To apply these techniques
Need to have:
a modelling language for networks
a specification language for correctness
a system, data structures to encode program and data and a solver
Examples:
state machines, Datalog, Propositional Logic
CTL, Modal Logic, Datalog
NuSMV using BDDs or IC3 for routers and packets SMT solver (Z3) for checking logic formulas

## Slide 25: Reactive System/State Machine
– set of states
– set initial states
– transitions
Runs:
Computation Tree:
describes edges in a tree
of all behaviors.

## Slide 26: A Sample Network N1
A
B
D
src:10* dst: 01*
src:1** dst:***
src:10* dst:***
src:*** dst:1**
src:1** dst:***; dst[1] := 0
R1
R2
R3
Program: Packets matching source IP 101 or 100, and destination IP 010 or 011 are forwarded from R1 to R2
States: Headers at Ports : (h, p)
Initially: All possible packets is at Port A
State Transitions: Router forwarding rules move packets between ports

## Slide 27: Networks as Reactive Systems
- output ports
- node + out port
- link to next node
Such that
- - is a set packet injection points

## Slide 28: CTL Specifications
A for all branches, E for some branch.
F if one some state in branch, G for all states in branch
x,y
x
x
x, y, z
y
E F z
A F y
E G x
Example: Al-Sharer 2010: VoIP phones cannot communicate with laptop

## Slide 29: Model Checking Encoding of N1
A
B
D
10* 01*
1** ***
10* ***
*** 1**
1** *** dst[1] := 0
Which packets can reach B from A?
Check
- “EF”: There exists a path such that …

## Slide 30: Model Checking Evolution
Explicit Model Checking: Works for protocols, doesn’t scale directly to many state bits
Symbolic Model Checking: Works on sets of states encoded compactly with BDDs
Bounded Model Checking: Unrolls state machine k times and uses SAT solver to verify or find counterexample
Impact, IC3 (interpolants, inductive properties): Search for inductive invariants using SAT/SMT solvers

## Slide 31: Binary Decision Diagrams
From A. Ragunathan, Purdue University

## Slide 32: BDDs for Networking Folks
Compact encoding for Boolean Functions (beyond SMC)
Examples uses:
  [Al-Sharer 10] : model router forwarding state machine
  [Yang 13]: model sets of headers
Pros:
  Compositional: Unions, Intersections, Canonical form
  Works well with some model checkers (NuSMV)
  Code Available: e.g., BuDDy , CUDD Library
  Generalizations to non-Booleans available
Con:
  Sensitive to variable ordering

## Slide 33: SAT and SMT as useful subroutines
SMT = SAT + Theories
SAT & SMT is at least NP hard!
But modern SMT solvers are very fast.
Can reduce network verification to SAT/SMT
Many good solvers, including Z3 .

## Slide 34: SAT in a nutshell
(Tie  Shirt)  (Tie  Shirt)  (Tie  Shirt)

## Slide 35: Satisfiability Modulo Theories (SMT)
Is formula  satisfiable modulo theory T ?
SMT solvers have specialized algorithms for T

## Slide 36
Arithmetic
Array Theory
Uninterpreted Functions
Satisfiability Modulo Theories (SMT)

## Slide 37
  This could be you
  if you use Z3

## Slide 38: Online @ rise4fun.com

## Slide 39
Available from GitHub

## Slide 40: Data Plane as Logic Circuit SAT [Malik]
Combinational Logic
Model it as a combinational logic circuit?
  Outputs and signals are functions of only the present value of the inputs
If so can use SAT solvers and not (harder) state machine verifiers
Network Formula:

## Slide 41: SAT Encoding of N1
A
B
D
10* 01*
1** ***
10* ***
*** 1**
1** *** dst[1] := 0
Which packets can reach B from A?

## Slide 42: Encoding reachable states with Datalog
Declare facts as predicates: Parent (john, aju), Parent (aju, tim)
Declare inference rules: Head holds if body
  Ancestor (X, Y) :- parent (X, Y)
  Ancestor (X, Y) :- parent (X, Z), ancestor (Z, Y)
State queries ?- Ancestor (john, X)
System runs to a fixed point and returns all variables john is an ancestor of (aju, tim)
Useful if we can state analysis problem recursively and want all solutions not just one. Restrictions  eff. decision procedure

## Slide 43: Datalog Encoding of N1
A
B
D
10* 01*
1** ***
10* ***
*** 1**
1** *** dst[1] := 0
Which packets can reach B from A?

## Slide 44: Two Simple Demos
N1 encoded into Bounded Model Checking (SAT) and Datalog
using Z3’s Python API

## Slide 45: SAT Encoding of N1
A
B
D
10* 01*
1** ***
10* ***
*** 1**
1** *** dst[1] := 0
Which packets can reach B from A?

## Slide 46: Datalog Encoding of N1
A
B
D
10* 01*
1** ***
10* ***
*** 1**
1** *** dst[1] := 0

## Slide 47: First Order Logic (Flowlog  Alloy)
Flowlog [Nelson 2014] is a top down language for writing controller programs
Specifications in First Order Logic: ∀, ∃
  All packets on Port 1 will be NATed
  Packets from stolen laptop -> Police Notification
Uses Alloy to solve for counterexamples
Useful for higher level properties as in say controllers but
may have difficulty scaling  decision procedure for FOL over finite domains

## Slide 48: General SW/HW Verification Toolbox and Networking Examples
Model Checking
Program
Verification
Abstract Interpretation
Runtime Verification
Certified Development
Model Based Testing
Model Based Development
Symbolic Execution
(ex. Al-Shaer via CTL)
(ex. HSA)
(ex. NetCore -> OF)
(ex. ATPG, NICE)
( ?)
( e.g., ATPG)
( e.g., Vericon)
( ?)

## Slide 49: Beware the Black Box
 | Model Checker | SMT All Solutions | NoD | HSA
Stanford Unreach | 12.2 | 0.1 | 2.1 | 0.1
Stanford Reachable | 13.7 | 1121 | 5.9 | 0.9
Stanford Loop | 11.7 | 290 | 3.9 | 0.2
Cloud | Time out | Time out | 15.7 | -
Cloud 2 | 8.5 | Time out | 4.8 | -
Run time in seconds
Expressivity-run time tradeoff between hand-crafted code
and leveraging existing code

## Slide 50: Data Plane versus Control Plane
1.2.*
Accounting
1.8.*
Engineering
1.8.*
1.8.*
1.8.*
1.8.*
Data Plane (DP): Collection of forwarding tables and logic that forward data packets
Control Plane (CP): Program that takes topology and failed links into account to build forwarding tables for data plane
Existing vs SDN: CP distributed in routers (OSPF, BGP) or centralized (SDN)

## Slide 51: Verification Tasks [Fayazbakhsh 15]
Program types:
DP tasks for fixed snapshot of FIBS
CP verifiers for fixed configuration

## Slide 52: Examples
Program types:
  Control Plane: RIP, OSPF, BGP
  Data Plane: IP, MPLS, OpenFlow
Data Plane:
  f: IP Fowarding or Openflow Forwarding tables
  Φ: reachability, no loops, waypoint traversal
Control Plane:
  e: Route Announcements, Link Failures
  Latent Bugs: Information flow, backup differences

## Slide 53: DATA PLANE VERIFICATION: IF ONE COUNTEREXAMPLE SUFFICES
Introduction to Formal Methods
Data Plane Verification
One counterexample
All counterexamples
Optimizations
Adding Functionality
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 54: Historically: Encode networks using existing verification engines
[Xie05] Theoretical reachability algorithm
[AlShaer09]: Model checking approach
[Mai11]: SAT Based Anteater
If 1 counterexample + small networks, reusing existing tools works fine. Only clever encoding
SAT Based approach optimized by Malik et al. [Zhang13] whose formulation we describe

## Slide 55: FlowChecker [Al-Shaer 10]
Al-Shaer group has been using model checking for firewalls, networks for 10 years!
Flowchecker [Al-Shaer 10] applies ideas to SDN.
Routers as BDDs, specs in CTL, and NuSVM to check end-to-end specs for SDN controllers.
Small scale experiments. May not scale

## Slide 56: SAT Based Property Verification [Malik]
Property
Formula:
Network
Formula:
Satisfiability
of
Satisfiable:
Property violated
Unsatisfiable:
Property holds
Property Formula
  Encode negation of the property: finding counter examples
    Example: Check the reachability from A to B
    Property Formula: conditions for non-reachability
Counterexample

## Slide 57: Adapting Modeling/Analysis
  Limit packet flow to a single path for a single packet through the network
Loop
Multicasting

## Slide 58: Modeling/Analysis Challenge
  Even for a single packet entering a network, a link may see multiple packets
Loop
Multicasting
  Switch output not a combinational function of its inputs
IO-relation
Fixed-point computation
Need to store sets of values

## Slide 59: Adapting Modeling/Analysis
  Limit packet flow to a single path for a single packet through the network
Loop
  Captures only part of the network behavior
  What good is this?
Loops implicitly blocked

## Slide 60: Goal: Counterexamples for Property Failures
A
B
Packet
Slice 1
Slice 2
X
A
B
C
D
Suffices for
Functional Properties:
  Reachability checking
    Waypointing
    Blacklisting
Functional/Performance Properties:
  Forwarding loop
Security Properties:
  Slice isolation
    virtualization context
Single Path Single Packet Counterexample

## Slide 61: Adapting Modeling/Analysis
Non-deterministically select one of the paths
  choice variable
Solver explores all possibilities for counterexample
Multicasting
choice

## Slide 62: Adapting Modeling/Analysis
Pkt A: tag 0
Pkt B: tag1
Pkt from A: tag 1
Extra tag bit tracks looping
  Packets enter the network with tag 0
  Switch with two incoming packets:
    One of the two packets has looped
    Switch selects packet with tag 0 for forwarding
    The tag of output packet is 1
  Looping packet is blocked
  Minimally unroll to check for k-times-looping
Packet loops iff there exists a switch with two incoming packets
  Easy check for packet looping
Avoid maintaining full path history

## Slide 63: Zhang-Malik versus AntEater
Zhang-Malik more modular. Separates network and property formula
More efficient encoding for loops and reachability.
For example, loops are caught in Anteater by making two copies of every switch and checking if each switch can reach its copy.
Both: only 1 counterexample for reachability

## Slide 64: DATA PLANE VERIFICATION: IF ALL COUNTEREXAMPLES ARE NEEDED
Introduction to Formal Methods
Data Plane Verification
One counterexample
All counterexamples
Optimizations
Adding Functionality
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 65: Why all examples?
Easier to see which rule caused counterexample.
Easier to do incremental verification
However, we have now gone from SAT to AllSAT which modern SAT solvers are not optimized for.
Fortunately, we can exploit the domain structure to do quite well.

## Slide 66: Towards all Solutions: Header Space [Kazemian 12]
Step 1 - Model a packet, based on its header bits, as a point in {0,1}L space – the Header Space
Two abstractions: 1. All layers collapsed into a flat sequence of bits 2. Wildcards ignore header bits irrelevant to forwarding
01110011…1
L
Header
Data
0xxxx0101xxx
Notes: * More time on this – field  bits
The first step is to model a packet based on its header as a point in {0,1}L space, which we call the header space. The idea here is that we look at packet headers a a flat sequence of 0s and 1s, without any protocol specific meaning for those bits. We don’t care whether the 32 bits corresponds to IP source or destination. That’s related to protocols. Then based on value of those bits, we map the packet to a point in the header space. Here we need to choose L large enough to contain all bits in the header. Similarly, a flow that has some wildcard bits in it, will corresponds to a region in the header space. Like Fourier transform in communication systems, the header space representation give us a simple and unified view of all packets.

## Slide 67: Header Space Framework
Step 2 – Model all networking boxes as transformers of header space
Packet
Forwarding
1
2
3
0xx1..x1
Match
+
Send to port 3
Rewrite with 1xx011..x1
Action
11xx..0x
+
Send to port 2
Rewrite with 1x01xx..x1
1110..00
1101..00
Transfer Function:
Notes: The second step is to model all networking boxes as transformer of header space. Here I am showing a simple packet forwarding element consisting of 3 ports, and I also show the header space corresponding to each port. We know that we can represent the forwarding functionality of this box by a set of rules. Each rule consists of a match which tell us which packets match on this rule and an action which tell us how the matching packets are sent to output. The match basically corresponds to a region in the input port header space and the action shows how that region is transformed to output. Similarly if we have more rules, we will have more match regions that is transformed to output header space….

## Slide 68: Transfer Function Example
IPv4 Router – forwarding + TTL + MAC rewrite
  172.24.74.x Port1
  172.24.128.x Port2
  171.67.x.x Port3
1
3
2
(rw_mac(dec_ttl(h),next_mac) , 1) if dst_ip(h) = 172.24.74.x
(rw_mac(dec_ttl(h),next_mac) , 2) if dst_ip(h) = 172.24.128.x
(rw_mac(dec_ttl(h),next_mac) , 3) if dst_ip(h) = 171.67.x.x
T(h, p) =

## Slide 69: Composition, Inversion
T1(h, p)
R1
R2
R3
Theorem: Network behavior = composition of router transfer functions (Compositionality)
Theorem: given header h at destination p, we can invert to find (h’,s): headers sent at source s’ to produce (h,p) (Inversion)
Notes: * Tell them that previously people had to log into boxes, understand different notion, from different protocols and different vendors.
By composing transfer functions, we can find the end to end behavior of networks and the faith of packets as they traverse in the network. Let’s look at one example. Consider this packet arriving at box R1. by applying the transfer function of R1 to the packet, we can see the packet reaches to R2. we then apply the transfer function of R2 to the result, and see the packet reaching R3. repeating the same process, we can see that applying the transfer functions sequentially to the input packet, which is equivalent to composing those transfer functions, will show the faith of the packet after going through the network.
Therefore, for packet between these two ports, we can model the forwarding behavior of the network by a black box, withT3T2T1 transfer function. Remember that without this mechanism, we had to log into every box and comprehend the overall behavior from different tables running different protocols and belonging to multiple vendors.

## Slide 70: Header Space Algebra- Intersection
Bit by bit intersect using intersection table:
  Example:
  If result has any ‘z’, then intersection is empty:
  Example:
wildcard
empty

## Slide 71: Computing Reachability
All Packets that A can use
to communicate with B
All Packets that A can possibly
send to box 2 through box 1
All Packets that A
can possibly send
Box 1
Box 2
Box 3
Box 4
A
B
T1(X,A)
T2(T1(X,A))
T4(T1(X,A))
T3(T2(T1(X,A)) U T3(T4(T1(X,A))
T-13
T-13
T-14
T-12
T-11
T-11
All Packets that A can
possibly send to box 4
through box 1
Notes: The first problem we want to look at, is finding reachability between two hosts in the network. We want to find out whether A can talk to B and if so, what are all packet header that will reach B.
To do that, we start by injecting test packet with wildcard in all bit positions into this simulated network. An all-x test packet is a packet whose bits are all wildcarded, and it represent the set of all possible packet headers that A can generate.
I want to emphasize that we don’t actually send any packet in the actual network, we get a complete snapshot of network and generate transfer function for each box in the network and use it for our analysis.
We apply the all-x packet to the transfer function of box 1, and gets some header space regions passed through the box, so we get the headers at the output of box1. we then apply the result to second transfer function – get the output header space after 2 hops, and finally to the 3rd transfer function giving us the ultimate results….

## Slide 72: Reachability via ternary simulation
  Worked terribly till we introduced compression via difference of cubes: ∪ wi − ∪ wj.
  And many optimizations: lazy evaluation (400x), dead space elimination  10,000x speedup
  We found difference of cubes worked better and faster than BDDs but jury is still out
  Difference of cubes seems to work because router “formulae” have 1 level of negation
  R1: 100* P1, R2: 1*  P2, becomes . . .
  Generalizes to path predicates, secure slicing . . .
STRUCTURE IN DOMAIN: LIMITED NEGATION, SMALL SET OF FORWARDING
EQUIVALENCE CLASSES, LIMITED REWRITES, NO LOOPS, SMALL DIAMETER
Notes: … Now if we want to see if the returned header space region will loop in the next round or not, we should apply the inverse of transfer function to trace the returned header space back to its origin and find out what part of the original all-x test packet could generate the loop. We call this the original header space and the blue region, the returned header space. The idea here is that, from all packet headers, only this orange region can generate loop, and it will come back to injection port in the form of this blue region.

## Slide 73: Run Time Compression via Difference of Cubes
10*
110
1**
Two keys to compression:
Distributivity: On matching 110, (1** - 10*) 110 = 110 - = 110
Cancellation: (1** - 10*) 10* = 10* - 10* = . If each positive header space is subsumed by a negative (cheap check), then
1** - 10*
10*
110*

## Slide 74: Secure Slicing of Networks
Network slice of resources defined by
  A topology consisting of switches and ports.
  A set of predicates on packet headers.
Think Citibank & BOA sharing network.
Generalizes what are known as VLANs today
Notes: * Slicing is a step to virtualization like bank of america and city want to share the same infrastructure. Like we do it for software. Once you do that, like VMs where we don’t want to interact, we want the same thing here- also there is security.
Next algorithm we discuss is checking isolation of slices, but first we should define what do we mean by a network slice.
A slice is a piece of network resources defined by a topology, consisting of a set of switches and ports the belong to that slice.
And a set of predicates on packet headers that is controlled by that slice. We could have potentially one predicate per switch or port.
As an example, if we want to create a VLAN slice on these switches, then the definition of slice will look like this – on each switch belonging to the slice, we have a header space corresponding to the slice predicate. We call this the header space definition of the slice.

## Slide 75: Checking Isolation of Slices
How to check if two slices are isolated?
  Slice definitions don’t intersect.
  Packets don’t leak after forwarding.
Notes: * The intellectula thing is thatw e don’t need to do it end to end – we do a one hop check.
Now let’s get back to the original question – how to check if two slices are isolated?
Let’s imagine in this example network, we have a red slice defined as shown. The first check, is to make sure that slice definitions don’t intersect. We can use intersection operation of HSA to this check. The red and blue slice pass this check.
The second check is to make sure that packets don’t leak after forwarding. To check for that, we apply the header space definition of each slice to the transfer function of network, to find the image of slice under network transformation, and that image should not intersect with any other slices, because the image shows us how packets in one slice will look like after one hop of forwarding. In this case, they do, and therefore the two slice are not isolated.

## Slide 76: DATA PLANE VERIFICATION: OPTIMIZATIONS
Introduction to Formal Methods
Data Plane Verification
One counterexample
All counterexamples
Optimizations
Adding Functionality
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 77: Scaling to Large Networks
Exploit:
Incrementality [Kazemian 13, Horn 17]
  Only small parts of program change on rule change
Local Checking [Jayaraman 15]
  Suffices in structured data centers
Equivalence Classes [Khurshid 13, Yang 13]
  Number of header equivalence classes is small
Symmetries [Plotkin 15]
  Many rules and boxes are repeated (redundancy)
Slices [Panda 17]
  Traffic only touches subset of network
  Forwarding is agnostic to source of traffic

## Slide 78: Exploiting incremantality: NetPlumber [Kazemian 13]
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
S
?
VERIFYING CHANGES BY SDN CONTROLLERS BEFORE THEY TAKE EFFECT

## Slide 79: Verifying Local Forwarding Rules with just Z3 (No propagation)
Contract
Logic
Routes
Local check only
[Jayaraman 15]

## Slide 80: Scaling via Equivalence Classes
Verification complexity proportional to number of headers and rules.
But number of equivalent header classes should be small [Lakshman 98]
Two strategies to discover: Veriflow (heuristic) and Atomic Predicates (optimal)
Similarly, many redundant rules in backup routers (exploit symmetry)

## Slide 81: Computing Equivalence Classes in Veriflow [Khurshid 13]
(device, rule) pairs
(don’t care/wildcard)

## Slide 82: Atomic Predicates Intuition [Yang 13]
From run-time compression via Difference of cubes to precomputed compression via Ai
Computes pairwise intersection of router and ACL guards to generate Ai using BDDs
Then rewrites forwarding rules using a simple set of integer labels for each
Symbolic propagation  propagating sets of integers. Fast. No rule matching, less space
Analog to MPLS versus IP forwarding!

## Slide 83: Atomic Predicates
Compute a set Ai of non-empty sets of headers:
The union of all the Ai covers all headers
The Ai are disjoint (no header in common)
Each predicate in a forwarding rule can be written as the union of a subset of the Ai *
Example: 1* R1, 10* R2, 110* R3. Then A1 = 0*, A2 = 10*, A3 = 110*, A4 = 111*
Our MS data centers have < 10K of Ai
* [Yang13] takes into account next hops as well

## Slide 84: Compile Time Compression via Atomic Predicates
10* {2}
1** {3,4}
Keys to compression:
Labels not prefixes: Every guard and header set  set of integers
Propagation: On match, do intersection. No prefix matches!
Limitation: Original paper assumes no header rewrites by routers
{3,4}
10*{2}
{3}
110 {3}

## Slide 85: Router Rules Venn Diagrams ddNF
1**
*1*
11*
Original guards
Forwarding rules
1** via port1
*1* via port2
**1 via port3
*** via port2
Intersection
**1
*11
1*1
111
***
1**
*1*
11*
**1
1*1
*11
111
  SG3 datacenter:
  ~200 routers, 1K rules each,
  but <10K disjoint address ranges
[B, Juniwal, Mahajan, Seshia, Varghese HVC 2016]

## Slide 86: Exploiting Symmetry [Plotkin15]
Can exploit regularities in rules and topology:
Symmetry Theorem: Can reduce fat tree to “thin tree” using a “simulation” and verify reachability cheaply in latter
Symmetry

## Slide 87
Methodology
Create models of middleboxes
Compose with network configuration
Exploit domain insights to slice the network
Check temporal (safety) properties
Reduction to decidable logics
What
Network reachability in the presence of stateful middle-boxes
Domain insight
Flow Parallelism: flows can be analyzed in isolation
Origin Agnostic: forwarding typically does not depend on where/how packet was received

## Slide 88
What
Detect network reachability problems in real time on the Dataplane
Domain insight
Many packets behave the same on a (large) subset of a network.
Methodology
Introduce new atoms, corresponding to equivalence classes of packets.
Network updates are handled incrementally.

## Slide 89: DATA PLANE VERIFICATION: ADDING FUNCTIONALITY
Introduction to Formal Methods
Data Plane Verification
One counterexample
All counterexamples
Optimizations
Adding Functionality
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 90: Improving Functionality
Support for dynamic networks and imperfect specifications (NOD)
  HSA only static specifications, static routers
Support for Quantities (Sung09)
  HSA only verifies Boolean properties
Support for Stateful boxes
  HSA does not handle stateful boxes like NAT etc.

## Slide 91: Dynamic Networks: Network Optimized Datalog [Lopes15]
Classical model checking provides languages based on temporal logic to specify a variety of properties
  Header Space hard codes some properties
  Classical verification tools compute only 1 solution
  Datalog computes all but was inefficient. Had to redo Datalog engine
Datalog nearly as fast as HSA but much more expressive
Included in Z3. Part of Batfish checker.

## Slide 92: Quantitative Verification [Sung 09]
Extends verification to non Boolean quantities such as Class of Service
Especially important in ISPs: differential treatment of traffic, marking, queues, rates
Finds all class of service treatments for any flow F a user queries for
Like reachability, accumulate QoS actions in path
Uses BDDs to model QoS ACLs. Finds bugs based on QoS “beliefs”

## Slide 93: Recursive ruleset representation of a policy block
Q1
Q2
Q3
Q
class-map match-any REALTIME
match access-group VOICE
match access-group INTERACTIVE-VIDEO
match ip dscp 46
class-map match-all CRITICAL-DATA
!
policy-map WAN-EGRESS-POLICER-QUEUE
class REALTIME
priority percent 35
class CRITICAL-DATA
bandwidth percent 40
class class-default
bandwidth percent 25
!
interface Serial1/0 ! INTERFACE TO PE1
service-policy output WAN-EGRESS-POLICER-QUEUE
!
ip access-list extended VOICE
permit ip 192.168.1.0 0.0.0.255 any
permit ip any 192.168.1.0 0.0.0.255
ip access-list ...
VOICE
INTERACTIVE-VIDEO
REALTIME | CRITICAL-DATA | output
match | * | Q1
* | match | Q2
* | * | Q3
VOICE | INTERACTIVE-VIDEO | IP marking | output
permit | * | * | match
* | permit | * | match
* | * | 46 | match
* | * | * | no
srcIP | srcPort | destIP | destPort | proto | output
192.168.1.0/24 | * | * | * | * | permit
* | * | 192.168.1.0/24 | * | * | permit
* | * | * | * | * | deny
*=Don’t care

## Slide 94: Example query
CE1
PE1
PE2
Core
S
To CE2
CE2
M2
M3
M4
Pm
Tx
P2
Tx
Tx
P3
P4
Qm
Q2
Q3
Q4
mpls:4
mpls:4
mpls:3
Q(C3)
Q(C4)
Q(C2,Cm)
Mx, Px, Qx: marking, policing, queuing rules for class Cx
Tx: transmit the flow without taking any action
Cm: network management class
Data classes: C2, C3, and C4
SF

## Slide 95: Stateful boxes as transducers [Sagiv 2015]
Stateless: S = {s0}
Increasing:
Progressing: only loops are self-loops
Arbitrary
Progressing
Increasing
Nat
Learning Switch
Firewall
IDS
Cache
Load Balancer
Stateless
P
co-NP Complete
EXP-Space Complete

## Slide 96: Road Map
Introduction to Formal Methods
Data Plane Verification
Control Plane Verification
Data Plane Testing
Control Plane Testing
Synthesis, Semantics

## Slide 97: CONTROL PLANE VERIFICATION
Introduction to Formal Methods
Data Plane Verification
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 98: Earlier Control Plane Work
BGP Loops Possible
  [Govindan, Griffin-Wilfong]
Sufficient Conditions for Avoiding Loops
  [Gao-Rexford]
Route redistribution can cause loops
  [Le 2008]
But based on human analysis and proofs. We now describe some tools for automated analysis

## Slide 99: Static Checking BGP Configs: RCC [Feamster 05]
Checks BGP configs for path visibility, validity
Example, route reflector configuration bugs
Route r (not visible to all)
Route s (visible to all)

## Slide 100: CP Tester: BatFish [Fogel 15]
  Check configuration sanity before applying to the network
    Check safety in the presence of certain routing changes
    Check back-ups are properly implemented
    Abstractions: Datalog model, ignores race conditions
Config files
Control plane logic
Data plane state
Parser
Logic solver
Query
Query solver
Provenance
Environment

## Slide 101: VeriCon [Ball 14]
Works for infinite state systems. All networks that meet network invariants
Works only for safety properties
Needs auxiliary invariants for proof
  but system uses weakest preconditions to supply hints

## Slide 102: SDN Control Programs Proved
Program | Program and Property
Firewall | Correct forwarding for a basic firewall abstraction
MigFirewall | Correct forwarding for a firewall supporting migration of “safe” hosts
Learning | Topology learning for a simple learning switch
Resonance | Access control for host authentication in enterprises
Stratos (Simplified) | Forwarding traffic through a sequence of middleboxes
Notes: * The first three are the basic application proposed for SDN, the later two are real and industry accepted applications.
* VeriCon is sometimes comparable to existing verification systems and in others faster
* VeriCon achieves significantly stronger guarantees as it proves the correctness on all possible topologies and network events.

## Slide 103
Check reachability invariants of routes created by BGP, OSPF.
Domain insight
Cut the middle-man: Can check reachability directly on policies without generating dataplane.
Methodology
ARC (Abstract Representation for Control planes) extracted from policies.
Capture path priorities, possible paths.

## Slide 104
What
Verify properties of BGP configurations
Domain insight
BGP policies describe flows at a stable state [Tim Griffin 2002].
Encode what it means for a state to be stable.
Check properties over these.
Methodology
Encoding of policies into fixed-point equalities.
Slice fields and bits away that don’t matter.

## Slide 105: DATA PLANE TESTING
Introduction to Formal Methods
Data Plane Verification
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 106: Symbolic Execution Methods
Want to push program to as many states as possible: maximize coverage
Random (Fuzz testing) useful but can do better.
Idea: Encode program as a decision tree. Try to cover all paths in decision tree

## Slide 107
int BadAbsoluteValue(int x)
{
if (x < 0)
return – x
if (x == 1234)
return – x
return x
}
X < 0?
X = 1234
X = *
Return - X
TRUE
FALSE
TRUE
Return - X
Return X
(Test cases: x = -3, x = MIN_INT)
(Test case: x = 1234)
(Test case: x = 500)
These three tests have 100% coverage in this case. A constraint solver supplies concrete values for each path

## Slide 108: Scaling Symbolic Execution
General idea: model each path and decision as a conjunction of constraints
Constraint solver: generate concrete values for each explored path that is tested
For large programs with loops, use heuristics to pick branches to maximize line coverage
Abstract OS calls like to File System and Disk. Provide mock framework to abstract OS calls
Some publicly available tools: Klee & Pex

## Slide 109: Symbolic Execution
Execution Path
Run Test and Monitor
Path Condition
Unexplored path
Solve
seed
New input
Test Inputs
Constraint System
Known Paths
Pex (unlike Klee) starts with a concrete input as seed and then solves constraints to explore other paths.
SMT solver

## Slide 110: ATPG vs Klee [Zheng 13]
Monitor the data plane by sending test packets.
  Maximum rule coverage (like Klee: rules lines)
  Minimize number of packets required (like Klee: packets test cases)
  Constraints on terminal ports and headers of test packets (unlike Klee)
Once error is detected, localize it (unlike Klee more like tomography)

## Slide 111: Example
rA1: dst_ip=10.0/16 → Port 0
rA2: dst_ip=10.1/16 → Port 1
rA3: dst_ip=10.2/16 → Port 2
rB1: dst_ip=10.2/16 → Port 2
rB2: dst_ip=10.1/16 → Port 1
rB3: dst_ip=10.0/16 → rB4
rB4: tcp=80 → Port 0
PA
0
1
2
PB
PC
0
1
2
0
1
2
rC1: in_port=1 → Port 0,2
rC2: in_port=0,2 → Port 1
Box A: Router
Box C: L2 Switch
Box B: Router+ACL

## Slide 112: Step 1: Find all-pairs reachability
PA
PB
PC
Box A
Box C
Box B

## Slide 113: Step 2: Find minimum covers
PA
PB
PC
Box A
Box C
Box B
Cover All Rules

## Slide 114: Step 2: Find minimum covers
PA
PB
PC
Box A
Box C
Box B
Cover All Links

## Slide 115: Step 3: Localize fault
PA
PB
PC
Box A
Box C
Box B
Cover All Links
P1
P2
P4
P3

## Slide 116: How many packets suffice?
<1% Link Utilization
when testing 10 times per second!
 | Stanford | Internet2
Total Packets | 621,402 | 3,037,335
Regular Packets | 3,871 | 35,462
Min-Set-Cover Reduction | 160x | 85x
Packets/Port (Avg) | 12.99 | 102.8

## Slide 117: Using ATPG for Performance Testing
Beyond correctness, ATPG can also be used for detecting and localizing performance problems.
Intuition: generalize results of a test from success/failure to performance (e.g. latency or bandwidth).
Track test packet latency/inferred bandwidth. Raise an error when changed significantly.

## Slide 118: Huh? Why is ATPG so simple
Because the size of the state space is bounded by network graph so simple set cover suffices
If, however, we have issues with scale (large networks) or imprecision, may need them
We also use ATPG less to find bugs in code than to do performance regression testing

## Slide 119: Software Data Plane Verification [Dobrescu 14]
Verifies actual code of Click software router.
Checks for new physical bugs (e.g., crash freedom, loops) using symbolic testing.
No path explosion: since router is a pipeline only compose potentially buggy path fragments
Use verified data structures (no pointers). Tradeoff verification ease with runtime cost.
Found bugs: e.g., IP option + fragmentation.

## Slide 120: Avoiding Path explosion and pointer analysis
IP Forwarding
ACL
QoS
Trie
IP Forwarding
ACL
QoS
Safe Table
m3 paths
3 m + 2 paths

## Slide 121
Domain specific language (DSL) for symbolic execution of SDN programs (including Click)
Domain insight
For SDN what matters is the branching of possible flows not the branching of a program.
The SymNet DSL captures flow behaviors.
Methodology
Dijkstra-ish calculus for networking DSL.
Mapping into SMT.

## Slide 122: CONTROL PLANE TESTING
Introduction to Formal Methods
Data Plane Verification
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 123: Control Plane Testing
Ex 1: Can we uncover latent bugs in BGP configurations before they show in dataplane
Ex 2: Can we do the same for OpenFLow controller code?
We will find now that symbolic testing methods are essential unlike in ATPG

## Slide 124: Ex 1: Catching an example BGP bug before it happens
Core
management network
C
B
E
A
D
1. A static rule was already present at B to provide access to the management network:
static route 1.2.3.0/24 0.0.0.0
2. B advertised this route to its BGP peers (including A):
network 1.2.3.0/24
3. A happened to contain a static route of the form:
static route 0.0.0.0/0 1.2.3.4 (Note: E did not have such a rule.)
4. A rejects the default route advertised by B :static default route takes precedence.
5. D does not receive default route from A and hence cannot forward via A when E fails
1.2.3.4
1.2.3.0/24
0.0.0.0/0
BGP peering

## Slide 125: Symbolic Testing for BGP Backup Router Equivalence [Fayazbakhsh 15]
Query: Is there any RIBoutBneighbor from B such that:
TAD(RIBoutBneighbor ) ≠ TED(RIBoutBneighbor )
Core
management network
C
B
E
D
A
The answer to this will be a RIBin containing 0.0.0.0/0.

## Slide 126: Snippets of router model in C
router transfer function
a route

## Slide 127: Unifying Routing (BGP, OSPF)
…
…
…
“Route” as the abstract data unit allows control plane unification across protocols.

## Slide 128: Setting up KLEE
invokes the abstract router model
static default route
on router A learned from config. file
a symbolic route
declaring the prefix field of the symbolic route as symbolic

## Slide 129: Using Klee to generate latent bug
An example scoping rule: Even though real routing protocols have many possible values for administrative distance (e.g., 256 value on Cisco), all we really need is distinct numerical values to differentiate protocols we use (6 protocols in our model)!
the symbolic route
router Id
scoping the ad field of the symbolic
verification query as a KLEE assertion (i.e., A and E have equivalent outputs)
Given the assertion (i.e., the klee_assert statement), the KLEE engine in this example will find a counter example. sym_route.prefix = 0

## Slide 130: Ex 2. NICE: Testing Open Flow Controller Code [Canini 12]
Controller not Data Plane: Harder, many more state transitions, ATPG does not work
SDNs: allow more programmability but also more bugs
Have to model hosts as well as asynchrony (Spec lax about service times of OF messages)
Found 11 bugs in existing NOX applications

## Slide 131
http://code.google.com/p/nice-of/
NICE: automated testing of OpenFlow Apps
Explores state-space efficiently
Tests unmodified NOX applications
Helps to specify correctness
Finds bugs in real applications
SDN: a new role for software tool chains to make networks more dependable.
NICE is a step in this direction!

## Slide 132: Combating Huge Space of Packets
Packet arrival handler
is dst broadcast?
Flood packet
Install rule and forward packet
dst in mactable?
Equivalence classes of packets:
Broadcast destination
Unknown unicast destination
Known unicast destination
yes
no
no
yes
Code itself reveals equivalence classes of packets
pkt

## Slide 133: Code Analysis: Symbolic Execution (SE)
Packet arrival handler
is λ.dst broadcast?
yes
no
Symbolic packet λ
Flood packet
λ .dst ∈ {Broadcast}
λ.dst in mactable?
no
yes
λ .dst ∉ {Broadcast}
Install rule and forward packet
λ .dst ∉ {Broadcast} ∧ λ .dst ∉ mactable
λ .dst ∉ {Broadcast}
∧ λ .dst ∈ mactable
1 path =
1 equivalence class of packets =
1 packet to inject
Infeasible from initial state

## Slide 134: Combining SE with Model Checking
New packets
Enable new transitions: host / send(pkt B) host / send(pkt C)
Symbolic execution of packet_in handler
State 0
State 1
Controller state 1
State 2
host discover_packets
State 3
host send(pkt B)
State 4
host send(pkt C)
discover_packets transition:
Controller state changes
host send(pkt A)

## Slide 135: SYNTHESIS AND SEMANTICS
Introduction to Formal Methods
Data Plane Verification
Data Plane Testing
Control Plane Verification
Control Plane Testing
Synthesis, Semantics

## Slide 136: Correct by Construction Synthesis
Synthesizing:
Virtual Networks [Rao 09]
Rules: Synthesize ACLs in routers based on network policy [Kang 13]
Tables across routers: NetCore to Featherweight Open Flow [Foster 13]
Tables within P4 router: [Jose15]
Single Firewall: [Zhang 13]

## Slide 137: VLAN Synthesis [Rao 09]
Network Core
.
.
.
.
H1
H2
H3
H4
Assign contiguous IPs to topologically separated hosts. Done manually today
Constrain broadcast costs
Limit routing inefficiencies
Data
Building1
Building2
Payroll VLAN
Sales VLAN

## Slide 138: Synthesizing VLANs
Goals:
Determine host membership of each VLAN
For each VLAN, find the best choice of root bridge and designated router
Correctness Constraint: Hosts in distinct logical categories (e.g., sales must belong to different VLANs
Feasibility Constraint: Limit total # of VLANs
Optimization objectives:
Minimize maximum broadcast traffic cost across VLANs
Minimize data traffic costs given traffic matrix
Optimization Technique:
Quadratic Semi-assignment/Facility Location
Heuristics work better on Purdue Network

## Slide 139: Rule Synthesis [Kang 13]
...
...
...
...
...
Automatic Rule Placement
Endpoint policy E
Routing policy R
Topology
Stay within capacity
Minimize total
1k
1k
0.5k
0.5k

## Slide 140: Three step greedy heuristic
H1
H2
H3
Step 2: Divide rule space across paths
Say Upper Path P1 has R2, R3, R4, R5, R7 and lower path has say R1, R6
Estimate total rules needed by each path, intuition: allocate more total rules to P1
Allocate per router rule budget using LP
Step 1: Partition global rules by paths
P1

## Slide 141: Step 3: For each path, Pick rectangle for every switch subject to rule budget
R7
R4
R3
R2
R5
5
3
1
R2, R3, R4’
R5 R3, R4’
R7

## Slide 142: Certified Development in NetCore [Foster 09]
Unlike one big switch, the input specification is modular: allows policies to be composed
P Q and P;Q. P can be atomic policies like filter or drop.
Motivates giving a denotational semantics.
Then provably compile from policies to open flow tables assuming no rule limits at routers.

## Slide 143: NetCore workflow [Foster 11]
Verified Compiler Theorem: Compiler Soundness
Verified Run-time system
Theorem:
Weak Bisimulation
Code Extraction

## Slide 144: NetKAT: Synthesis + Analysis in 1 package [Anderson 14]
NetKAT allows synthesis of policies and (unlike NetCore) allows automatic analysis of other properties besides policies synthesized.
Unlike Veriflow & HSA which verify a model NetKat allows analysis of code as written.
Denotational semantics and equational theory and shows completeness.
Equational theory used for certified development.

## Slide 145: NetKAT - calculus
pol ::= false
| true
| field = val
| pol1 + pol2
| pol1 ; pol2
| !pol
| pol*
| field := val
| S⇒T
Captures modeling SDN Dataplane
Suitable for algebraic toolsets
  Equation solving
  Check equality and inclusion between NetKAT programs using automata theoretic tools
Extensions:
  Probabilities
  stateful middleboxes

## Slide 146: Flowlog [Nelson 14]
Tierless programming for networks
  Compiler inserts controller communication
  Analysis enabled by SQL style language
  Supports stateful switches
FlowLog Program
Forwarding Behavior
Non-forwarding rules
Rules not supported by Switch tables
Forward to next hop
Forward to controller

## Slide 147: Synthesis using Solvers
Example 1: [Zhang12] uses Quantified Boolean Formulations to synthesize firewalls
  Uses binary search to scale
Example 2: [Jose15] uses ILP to synthesize physical tables within router from logical tables
  Uses model restrictions to scale
Either pure heuristics or solvers + heuristics needed as synthesis is hard.

## Slide 148: Synthesis via Verification Tools (don’t scale out of box)
Find an if one exists, such that for all, holds
Binary search for minimum k
Practical QBF (and special purpose) solvers do not scale well. Networks will be harder!
Packet
Symbolic
Firewall with
k rules
Firewall
Spec
Symbols
Quantified Boolean Formula (QBF)

## Slide 149
Synthsize global updates that avoid incorrect transient behavior
Domain insight
Space of update orders can be efficiently enumerated and pruned.
Update consistency expressible in LTL.
Methodology
Enumerate possible update conflicts.
Use incremental LTL model checker to check if update conflict is feasible.
Use counter-example to block set of remaining update conflict candidates.

## Slide 150
Domain specific language to write full network BGP policies
Domain insight
BGP policies (when used in a large AS) on each node capture some global intent that is better captured in a single policy language
Methodology
DSL with regular expressions built in to describe sets of (allowed) paths.
Compiler into local BGP policies

## Slide 151
Declarative DSL to configure policies
Synthesis procedure to extract configurations
Domain insight
Structure of Data-center networks can be captured using regular expressions.
This narrows space of configurations.
Methodology
Divide and conquer strategy for splitting search for valid configurations into parts.
Relies on SMT solving for feasibility and optimality queries.

## Slide 152
Methodology
Details of a network program are added in stages
Refinement steps are checked using an automatic model checker
What
Compile high-level description of network program to SDN programs (P4).
Domain insight
Network layers (VLANs, ACLs, L2/L3 routing) follow refinements

## Slide 153: LESSONS AND LOOKING BACK

## Slide 154: Research ideas?  via exemplars from research in real networks
IP Router
10010
ESSENTIAL INSIGHT FOR OPENFLOW. USE SAME INSIGHT
IN HSA FOR UNDERSTANDING EXISTING PROTOCOLS.
SIMILARLY MPLS  ATOMIC PREDICATES
10* P1
1*  P2
MAC Bridge
01A1A2
01A1A2 P1
. . .
PREFIX MATCH
EXACT MATCH
MPLS Switch
5, 6
5 P1,Pop 5
. . .
INDEXED LOOKUP

## Slide 155: Research ideas?  via exemplars from PL and Hardware Verification
Earlier Exemplar | Network Verification
Ternary Simulation, Symbolic Execution (Dill 01, Hardware) | Header Space Analysis (Kazemian 2003)
Certified Development of an OS Sel4 [Klein 09] | Certified Development of a Controller [Guha 13]
Specification Mining for HW [Li 10] | Mining for Enterprise Policy (Benson )
Exploit Symmetry in Model Checking [Sistla] | Exploit Symmetry in Data Center Verification (Plotkin15)
Can choose either analysis of existing (e.g., Veriflow) or clean slate
Approaches based on synthesis. Both have a place

## Slide 156: Exemplars: Food for thought?
What are Network Verification analogs of:
Abstract Interpretation (replacing complex state by a simple state)
CEGAR (counterexample driven refinement)
Interpolants
Strong typing in Language Design
Wiring checkers in Chip Design

## Slide 157: Scaling?  Exploit Domain Structure
Technique | Structure exploited
Header Space (HSA) | Limited negation, no loops, small equivalence classes
Net Plumber | Network Graph, rule dependencies structure
ATPG (Testing) | Network graph limits size of state space compared to KLEE
Exploit Symmetries | Known symmetries because of design (vs on logical structures)
Scope for Interdisciplinary work between PL, Hardware CAD, Verification Community and Networking Researchers

## Slide 158: No Specifications?  Use Beliefs
Paper | Example Beliefs
Bugs as Deviant Behavior [Engler 01] | Dereferencing Pointer P that could be NULL is a bug
Routing Config Checker (RCC) [Feamster 05] | Routes from a Peer should not be re-advertised to another peer
QoS Verification Tool for ATT [Sung 09] | Marked flows should be placed in corresponding queue
Network Optimized Datalog [Lopes 15] | Customer VMs should not be able to access router ports

## Slide 159: Don’t know how  Leverage code
SMT: CVC4, Mathsat, Yices, Z3
BDD packages: (BuDDy, CUDD)
Model checking: SPIN, nuSmv/nuXmv
Network Specific verification: Hassel, Veriflow, NoD, Eugene Chemeritskiy‘s fixed-point logic system, Atomic Predicates
Datasets: Stanford, Cloud (NoD), Internet2
Symbolic Test Generation: KLEE, DART, SAGE
Proof Assistants: Coq, Isabelle
Known to be available for download

## Slide 160: Network Design Automation? Lessons from EDA (Malik)
Design discipline for Network Design? (e.g, Fat Trees  Local Checks Only)
Design flows, abstractions and interfaces for Network Design? (SecGuru in Azure)
Effective modeling and analysis to enable NDA evolution? (Veriflow real-time checks)
Maximizing separation of concerns in Network Design? (Control and Data Plane)
Analysis capabilities influencing Network Design/Verification methodology? (Symmetry)

## Slide 161: Lessons Summarized
What research? Via exemplars from PL/HW
What research? Via exemplars from networks
Scaling? Exploit domain structure
Lack of specifications? Use Beliefs
Don’t know how? Leverage available code
Network Design Automation? Learn from EDA

## Slide 162: Conclusion
Inflection Point: Rise of services, data centers, Software Defined Networks
Ideas: Adapt Verification (analysis) & optimization (synthesis)
Intellectual Opportunity: Rethink existing techniques exploiting domain structure
Systems Opportunity Working chips with billions of gates Why not large operational networks next
Lot more than Verification and Formal Methods (debugging, simulation,
run-time checks, etc.) but EDA suggests this is an essential foundation
Notes: There is a lot more work. For example, we want hardware changes at routers for better monitoring and great debuggers that can do things
Like Step and Walk. But the techniques in this tutorial are a lot more than understanding existing bugs. They may help us lay a foundation
for a systems opportunity: the chance to change the way large networks are operated. The sky’s the limit: Destination Moon

## Slide 163: So what can we steal/adapt from the PL Toolbox?
Transition Systems
Language Based
Language Based
Semantics Based
Algebraic
Property Checking
State Exploration
Program Equivalence
(e.g., NetCore Policies)
(e.g., Lightweight Open Flow)
(e.g., Model Checking,
Header Space Analysis
(e.g., Model routers as
State machines)

## Slide 164: Data Plane Verification
[Lakshman 98] High-speed policy-based packet forwarding using efficient multidimensional range matching. Lakshman Stiliadis 1998
[Xie 05] On static reachability analysis of IP networks Xie, Zhan, Maltz, Zhang, Greenberg, Hjalmtysson. INFOCOM 2005
[Al-Shaer 09] Network configuration in a box: Towards end-to-end verification of network reachability and security Al-Shaer, Marrero, El-Atawy, Elbadawi. ICNP 2009.
[Sung 09] Modeling and understanding end-to-end class of service policies in operational networks Sung, Lund, Lyn, Rao, Sen, SIGCOMM 2009
[Al-Shaer 10]: FlowChecker: configuration analysis and verification of federated openflow infrastructures, SafeConfig '10
[Nelson 10] The Margrave Tool for Firewall Analysis Nelson, Barratt, Dougherty, Fisler, Krishnamurthi; LISA 2010
[Mai 11]: Debugging the Data Plane with Anteater Mai,Khurshid, Agarwal, Caesar, Godfrey, King. SIGCOMM 2011
[Kazemian 12] Header Space Analysis: Static Checking for Networks. Kazemian, Varghese, McKeown. NSDI 2012
[Kazemian 13] Real Time Network Policy Checking Using Header Space Analysis. Kazemian, Chan, Zeng, Varghese, McKeown, Whyte. NSDI 2013
[Khurshid 13] VeriFlow: Verifying Network-Wide Invariants in Real Time [NSDI 2013, HotSDN 2012]
[Zhang 13]: SAT Based Verification of Network Data Planes, Zhang, Malik. ATVA 2103
[Dobrescu 14] Network Dataplane Verification. Dobrescu, Argyraki. NSDI 2014.
[Chemeritskiy 14] VERMONT - a toolset for checking SDN packet forwarding policies on-line. Altukhov, Chemeritskiy, Podymov, Zakharov SDN&NFV conference 2014.
[Jayaraman 15] Automated Analysis and Debugging of Network Connectivity Policies. Jayaraman, Bjorner, Outhred, Kaufman
[Plotkin 15] Scaling Network Veriﬁcation using Symmetry and Surgery. Plotkin, Bjorner, Lopes, Rybalchenko, Varghese

## Slide 165: Control Plane Verification
[Feamster 05] Detecting BGP Configuration Faults with Static Analysis. Feamster, Balakrishnan. NSDI 2005
[Ball 14] VeriCon: Towards Verifying Controller Programs in Software-Defined Networks. Ball, Bjørner, Gember, Itzhaky, Karbyshev, Sagiv, Schapira, Valadarsky. PLDI 2014
[Nelson 14] Tierless Programming and Reasoning for Software-Defined Networks Nelson, Ferguson, Scheer, Krishnamurthi; NSDI 2014
[Fogel 15] A General Approach to Network Configuration Analysis, Fogel, Fung, Pedrosa, Walraed-Sullivan, Govindan, Mahajan, Millstein. NSDI 15.
[Nelson 15] Static Differential Program Analysis for Software-Defined Networks Nelson, Ferguson, Krishnamurthi; FM 2015
[Padon 15] Decentralizing SDN Policies Padon Immerman, Karbyshev, Lahav, Sagiv, Shoham. POPL 2015
[Foster 15] A Coalgebraic Decision Procedure for NetKAT Foster, Kozen, Milano, Silva, Thompson. POPL 2015

## Slide 166: Synthesis/Compilation
[Sung 08] Towards systematic design of enterprise networks Sung, Rao, Xie, Maltz. CoNEXT 2008
[Foster 11] Frenetic: A Network Programming Language Foster, Harrison, Freedman, Monsanto, Rexford, Story, Walker. ICFP 2011.
[Zhang 12] Verification and synthesis of firewalls using SAT and QBF (ICNP), 2012 Zhang, Mahmoud, Malik, Narain
[Kang 13] “One Big Switch” Abstraction in Software-Defined Networks, Kang, Liu, Rexford, Walker. CoNEXT 2013
[Guha 13] Machine-Verified Network Controllers Guha, Reitblatt, Foster. PLDI 2013.
[Anderson 14] NetKAT: Semantic Foundations for Networks Anderson, Foster, Guha, Jeannin, Kozen, Schlesinger, Walker. POPL 2014.
[Jose 15] Compiling P4 Programs, Jose, Yan, Varghese, McKeown. NSDI 2015
[McClurg 15] Efficient Synthesis of Network Updates. McClurg, Hojjat, Cerny, Foster. PLDI 2015.
[Diekmann 15] Semantics-Preserving Simplification of Real-World Firewall Rule Sets. Diekmann, Hupel, Carle. FM 2015

## Slide 167: Testing
[Canini 12] A NICE Way to Test OpenFlow Applications, Canini, Venzano, Perešíni, Kostić, Rexford. NSDI 12.
[Zeng 12] Automatic test packet generation. Zeng, Kazemian, Varghese, McKeown CoNEXT 2012
[Fayaz 15] From Header Space to Control Space: Towards Comprehensive Control Plane Verification, Fayaz, Fogel, Mahajan, Millstein, Sekar, Varghese,
[Brucker 15] Formal firewall conformance testing: an application of test and proof techniques. Brucker, Brügger, Wolff. STVR 2015.

## Slide 168: State space exploration tools
Tool | What it does | 
SMV | Symbolic Model Verifier | McMillan
NuSMV | De facto symbolic model checker today | Cimatti
SPIN | Explicit state model checker (good for protocols) | Holzmann
Impact | Symbolic model checking algorithm based on interpolants and SAT | McMillan
IC3 | Symbolic model checking algorithm based on inductive generalization and SAT | Bradley
Klee | Symbolic state space explorer for C | Engler
SAGE | Dynamic symbolic execution engine | Godefroid
Pex | Dynamic symbolic execution for .NET | Tillmann, Halleux

## Slide 169: Logic toolbox
Tool | What it is | 
CTL | Computational Tree Logic Lets you specify properties of computations | 
LTL | Linear Time Temporal Logic Lets you specify with fairness assumptions | 
Datalog | Horn Clauses without function symbols Lets you define sets by induction | 
FO+TC | First order logic with transitive closure Lets you take transitive closure of binary relation | 
KAT | Kleene Algebra with Tests Lets you write down programs as a regular expression with conditional statements | 
Relational Algebra (in Alloy) | Similar to FO+TC but composition of relations is first-class | 

## Slide 170: Proof and specification assistants
Tool | What it does | 
Coq | Interactive proof assistant | Coquand +
Isabelle | Interactive proof assistant | Nipkow, Paulson
ACL2 | A Computational Logic proof assistant | Boyer, Moore
Alloy | Relational algebra specification environment | Jackson
PVS | Interactive proof assistant | Owre+

## Slide 171: Automatic theorem prover toolbox
Tool | What it does | 
Z3 | SMT solver | de Moura, Bjorner, Wintersteiger
Yices2 | SMT solver | Dutertre
CVC4 | SMT solver | Barrett
MathSAT4 | SMT solver | Griggio
MiniSAT | SAT solver | Een, Soerenson
Lingeling | SAT solver | Biere
BuDDy | BDD package | Lind
CUDD | BDD package | Somenzi

## Slide 172: Some Network Verification Tools
Tool | What it does | Based on | 
Margrave | Specification Environment | Alloy | Nelson, Krishnamurthi
AntEater | Bounded Model Checker | Yices | Godfrey
Hassel | Symbolic Execution, reachability | Ternary bit-vectors | Peymen
NoD/Z3 | Network optimized Datalog, reachability | Datalog + ternary bit-vectors | Lopes
NetKAT | Networks as Kleene Algebra | Automata Theory | Foster
VeriFlow | Incremental verification | Tries | Khurshid
NetPlumber | Path queries using regular expressions, incremental verification | Header Spaces, slicing, regular expressions | Kazemian
SecGuru | Semantic Differences of forwarding tables and firewalls | SMT/Bit-vectors | Jayaraman
VERMONT | Network Reachability, incrementality | FO + Transitive Closure, BDDs | Chemeritskiy

## Slide 173: Recent Developments in Network Verification

## Slide 174
What
Diagnose and fix bugs in SDN applications
Domain insight
SDN control can be captured by rule-based systems (NDLog)
Methodology
Encode an interpreter of NDLog in NDLog.
Then rules and data are symmetric.
Perform symbolic exploration of NDLog meta program.

## Slide 175
Check reachability properties in large data-center networks
Domain insight
Large data-center networks are actually small.
Many routers do the same (are backups of each-other).
Methodology
Detect symmetric routing tables and replace by a single representative.
Routes tend to be acyclic.
Can use bottom-up method (dynamic programming) to find equivalent routing table entries.

## Slide 176
Program repair by fixing Horn Clauses
Domain insight
Network Configurations expressible using interval and Boolean predicates.
Methodology
Pick a counter-example for unsolved clauses.
Augment failed clause using extra predicates from the repair domain.

## Slide 177
Update networks dynamically in response to events
Domain insight
Updates can be captured using data-structure Network Event Structures
Methodology
Instrument NetKAT to handle state